## Slide 1
\
WEEK 1 Graded Activity System Thinking
Copyright © 2020. Massachusetts Institute of Technology. All rights reserved
Type your name

## Slide 2
Sample answer

## Slide 3: Elevator System (Sample Answer)
The expected emergent function is to translate riders vertically through a building. The benefit is quick and convenient access to upper floors in a multi-story building.
Scenario: What is the issue and what role do you play?
I am the chief system officer at an elevator company. A newly deployed product is having trouble operating. It seems the car is not stopping at the right position relative to the door on the floor. The boss has asked me to investigate and make a recommendation.
What are the problems associated with emergence of function, performance, ilities, and emergencies:
The main problem is performance. The car stops, but not quite in the right place.
Elevator shaft
Constraints car
Simple Elevator
System Boundary
Cable drive
Moves car
Building frame
Carries loads
User
Commands floor
Elevator car
Supports user
What is the expected emergent function and benefit?
What are the important entities in the system and context? Describe using the visual representation.

## Slide 4
What are the pairs of entities that are related, what are the interaction and structure? Describe using the grid.
Pairs of components | Structure (connection, location or sequence) | Interaction (processes interacting directly, passing or sharing an operand)
User & Car | User stands on floor of car | Exchange loads
User & Cable Drive | User pushes floor buttons | Pass commanded floor signal
Shaft & car | Car moves within shaft | None in normal operation
Cable drive & car | Cable connected to top of car | Exchange loads
Building frame & shaft | Shaft built into building | Exchange loads
Building frame & cable drive | Cable drive built into building | Exchange loads
Elevator System (Sample Answer)

## Slide 5
Q1. How can you reason through entities and relations to better understand the problem?
The user commands a desired floor number and the cable drive turns and pulls on the cable that pulls on the car. The car ends up close to but not exactly at the desired floor.
Q2. Is there one or two system solutions that you would propose?
There are two potential problems – the drive is not being commanded right, or the cable is stretching an unanticipated amount. System solutions include: better calibration of the cable length and stretch; feedback of wheel position from cable drive; or feedback of car position near doorway.
Elevator System (Sample Answer)

## Slide 6
Submission: YOUR PROFESSIONAL SYSTEM

## Slide 7
Type your answer in this box
Scenario: what is the issue and what role do you play?
Type your answer in this box
What are the problems associated with emergence of function, performance, ilities and emergencies:
Type your answer in this box
System Boundary
What is the expected emergent function and benefit?
What are the important entities in the system and context? Describe using the visual representation, modify as needed (you can draw it in a paper, take a picture, and paste below). Read the tutorial for representing systems.
Entity Form
Entity Function
Entity Form
Entity Function
Entity Form
Entity Function
Entity Form
Entity Function
Entity Form
Entity Function
Do not include any information that would violate security, confidentiality, or intellectual property regulation.
Your professional activity system name

## Slide 8
What are the pairs of entities that are related, what are the interaction and structure? Describe using the grid.
Pairs of components | Structure (connection, location or sequence) | Interaction (processes interacting directly, passing or sharing an operand)
Do not include any information that would violate security, confidentiality, or intellectual property regulation.
Your professional activity system name

## Slide 9
Q1. How can you reason through entities and relations to better understand the problem?
Type your answer in this box
Q2. Is there one or two system solution that you would propose?
Type your answer in this box
Do not include any information that would violate security, confidentiality, or intellectual property regulation.
Your professional activity system name